# Learn ZWCAD Mechanical in a Day

Contents

Learn ZWCAD Mechanical in a Day	0

1.	Basic drawing, dimension, and symbols	1

1.1.	Set frame to A3 and 1:1	1

1.2.	Drawing a contour	1

1.2.1.	Draw the contour of a part through hole and shaft design	1

1.2.2.	Two methods to draw a hole	3

1.2.3.	Draw a chamfer	4

1.2.4.	Draw a projection	6

1.2.5.	Draw a hole array	7

1.3.	Dimension	8

1.3.1.	Dimension	8

1.3.2.	Symbol Dimension	11

1.3.3.	View Dimension	13

2.	Operational procedure of ZWCAD MECHANISM	14

2.1.	Fill in the title	14

2.2.	Part Builder for drawing standard parts:	16

2.2.1.	Draw basic graphics	16

2.2.2.	Add standard fasteners for mechanism	16

2.3.	Balloons dimension and fill out the BOM	18

2.3.1.	Dimension the balloons	18

2.3.2.	Fill in BOM	21

2.3.3.	Generate BOM	23

2.4.	Add technical requirements	24

3.	Command/abbreviated command list	26

# Basic drawing, dimension, and symbols

This manual introduces the basic drawing features of ZWCAD MECHANICAL to give users a general understanding of the drawing tools and dimensioning methods.

## Set frame to A3 and 1:1

Click Border Setup or enter a ZWMFRAMEINIT2 to bring up the dialog box of Frame Settings;

Select A3 as frame size, and 1:1 as ratio, click OK, Enter

The Frame Settings are now done.  The outcome is as follows:

## Drawing a contour

### Draw the contour of a part through hole and shaft design

Step 1:

Click Shaft Generator or enter ZWMSHAFT, Set the parameter as follows:

Click OK to draw the newly designed shaft

Select an appropriate location in the drawing for the shaft, as shown:

### Two methods to draw a hole

1. Draw a center hole:

Click Hole Shaft Design or input: ZWMHOLEAXIS;

Command: _ZWMHOLEAXIS

Input first point of hole or [Shaft/First diameter:100.00 /End diameter:100.00 /centerline extended Length:3.00 /Centerline:no]:f

Input start diameter:<100>20

Input first point of hole or [Shaft/First diameter:10.00 /End diameter:10.00 /centerline extended Length:3.00 /Centerline:no]:<Pick the center point in the left side>

Spaecify next point or [Shaft/input Angle/First diameter:10.00 /End diameter:10.00 /centerline extended Length:3.00 /Centerline:no]:<Pick the center point in the right side>

Command:

2.Draw a hole around:

Offset the center line 30 to the above and below, and then Break the extra lines as follows:

Click Mirror line or input: ZWMMIRRORLINE;

Command: ZWMMIRRORLINE

Select Axis of symmetry

Line or[Arc/Circle/eXit]<X>:

Next point:5

Next point:

Next point:

Line or[Arc/Circle/eXit]<X>:

### Draw a chamfer

Click Chamfer or input: ZWMFILLETLC

Enter the Setup and set as follows:

After setting, click OK to draw;

Do the same chamfer to other parts as follows, set the length as 3:

### Draw a projection

Click Hole-Shaft Projector or input: ZWMHSPROJECTOR

Set as follows:

According to the prompts in the command line, to select the center line, and the features points. After that, move the objects to a certain distance as follows:

Notice: Need to change one of the circle from Layer 0 to Layer AM_7

### Draw a hole array

Click the Hole Array or input: ZWMARRAYHOLE, set as follows:

The result is as follows:

## Dimension

### Dimension

Click Power Dimension or input ZWMPOWERDIM

Select two points to dimension, and then Enter. When the cursor becomes a pick box, select the dimension, in this case, it is 40.

Then the Enhanced dimensioning box will prompts. Add the diameter symbol as follows.

Proceed to dimension the edge contour of the part by adding tolerance to the dimension. Set as follows:

The result is as follows:

Proceed to dimension other areas of the part.

The result is as follows:

### Symbol Dimension

Click Surface Texture or input ZWMSURFSYM

Set as follows

The result is:

(2) Circlemark

Click Circle Mark or input ZWMCIRCLEMARK

Select the desired circle mark, and click OK

### View Dimension

Click Section Line or input ZWMSECTIONLINE

Directly pick the points and add the section line

# Operational procedure of ZWCAD MECHANISM

Here is the brief description of the general steps for users to mechanical designs with ZWCAD MECHANICAL and for them to develop an overall understanding of ZWCAD MECHANISM.

## Fill in the title

Input: ZWMTITLEEDIT

You can directly select one of the contents and input values into it, or you can right click it and then select Word library, where you can select the prepared content to fill in.

The result is:

## Part Builder for drawing standard parts:

### Draw basic graphics

Continue to mirror the part as following shown:

### Add standard fasteners for mechanism

Click All Parts or input ZWM_SPART_OUTN

Set the parameter as follows:

Click Export to place the bolt as follows.

In accordance with the steps above, draw a washer and a nut in order, trim the related line type. The final outcome is shown in the figure:

## Balloons dimension and fill out the BOM

### Dimension the balloons

Click Balloons or input ZWMBALLOON

Click Setting

Set it by default, then click OK twice, then you can specify the location to add the balloon as follows.

### Fill in BOM

After specify the location, then the following dialog box prompts up:

Click Pick Standard Part Data

Pick the part, then the information will be filled in automatically.

Repeat the steps for the others balloons.

### Generate BOM

Click BOM Data or input ZWMTOTALBOMEDIT

Right click to select Generate list or press Ctrl+S.

The result is as follows:

## Add technical requirements

Adding technical requirements for drawings is also one of the important elements in mechanical design.

Click the Technical Requirement input ZWMTECHREQUEST

Finally, the case is finished as follows:

# Command/abbreviated command list

| Operation name | Execution command | Simplified command (shortcut) |
| --- | --- | --- |
| Frame |
| Multi-frame Setup | ZWMFRAMEINIT2 | FRA2 |
| Title Editor | ZWMTITLEEDIT |  |
| Additional Editor | ZWMFJLEDIT |  |
| Parameter list Edit | ZWMCSLEDIT |  |
| Switch Frame | ZWMSWITCHFRAME |  |
| Switch Scale | ZWMSWITCHSCALE |  |
| Switch title | ZWMSWITCHTITLE |  |
| Switch BOM | ZWMSWITCHBOM |  |
| Switch Code List | ZWMSWITCHDHL |  |
| Switch Additional List | ZWMSWITCHFJL |  |
| Switch Parameter List | ZWMSWITCHCSL2 |  |
| Revision list | ZWMREVISIONLIST |  |
| Current Border | ZWMSTDANDARDC | SDC |
| Hole Chart | ZWMHOLECHART |  |
| Balloon/BOM |
| Ballons | ZWMBALLOON | BAL |
| Edit Balloon Style | ZWMEDITBALLOONSTYLE |  |
| Balloon Data Editor | ZWMEDITBOMROW |  |
| Align Balloon | ZWMALIGNBALLOON |  |
| Renumber balloons | ZWMRENUMBERBALLOON |  |
| Hide Balloons | ZWMHIDEBALLOON |  |
| Show Balloons | ZWMSHOWBALLOON |  |
| Collect balloons | ZWMCOMBINEBALLOON |  |
| Adding leader | ZWMADDLEADER |  |
| Removing leader | ZWM ADDLEADER |  |
| Generate BOM List | ZWMPARTLIST | PLT |
| Processing BOM Data | ZWMTOTALBOMEDIT | TBE |
| Dimension |
| Power Dimension | ZWMPOWERDIM | D |
| Multi-dimension | ZWMAUTODIM | DAU |
| Length dimension | ZWMLINEARDIM |  |
| Horizontal Dimension | ZWMHORIZONTALDIM |  |
| Vertical Dimension | ZWMVERTICALDIM |  |
| Aligned Dimension | ZWMALIGNEDDIM |  |
| Half-section Dimension | ZWMHALFALIGNDIM |  |
| Point-to-line Dimension | ZWMPTLINEDIM |  |
| Diameter Dimension | ZWMDIAMETERDIM |  |
| Radius Dimension | ZWMRADIUSDIM |  |
| Jogged radius Dimension | ZWMJOGGEDRADIUSDIM |  |
| Coordinate Dimension | ZWM_DIMORDINATE |  |
| Arc length Dimension | ZWMARCLENGTHDIM |  |
| Chain Dimension | ZWMCHAINDIM |  |
| Baseline Dimension | ZWMBASELINEDIM |  |
| Center mark | ZWMCENTERDIM |  |
| Angular Dimension | ZWMANGULARDIM | DAN |
| Leader Dimension | ZWMANGULARDIM | NO |
| Sheet thickness Dimension | ZWMTHICKNESSDIM |  |
| Chamfer Dimension | ZWMCHAMFERSYM | CHS |
| Dimension combination | ZWMDIMJOIN |  |
| Inserting dimension | ZWMDIMINSERT |  |
| Dimension alignment | ZWMDIMALIGN |  |
| Dimension check | ZWMDIMCHECK |  |
| Tolerances for query | ZWMDIMTOLQUERY |  |
| Symbols |
| Surface Textureure | ZWMSURFSYM | SF |
| Feature Control Frame | ZWMFCFRAME | FCF |
| Datum identifier | ZWMDATUMID | DTD |
| Feature identifier | ZWMFEATID |  |
| Datum target | ZWMDATUMTGT |  |
| Taper&slope symbol | ZWMTAPERSYM | TPS |
| Center hole | ZWMCENTERHOLE | CTH |
| Circle mark | ZWMCIRCLEMARK | BJ |
| Break symbol | ZWMBREAKSYMBOL | BRS |
| Elevation symbol | ZWMELEVSYM | EF |
| Welding symbol | ZWMWELDING | WE |
| Creating view |
| Section Line | ZWMSECTIONLINE | STL |
| Direction | ZWMVIEWDIRECTION |  |
| Detail view | ZWMDETAIL |  |
| Scale Area | ZWMSCAREA |  |
| Text processing |
| Text Annotation | ZWMDIMTEXT | DTT |
| Technical requirements | ZWMTECHREQUEST | TRT |
| Drawing tools |
| Smart line | ZWMINTELLIGENTLINE | SS |
| Circle (Cen) | ZWMCIRCLEBYC | CBC |
| Circle (3P) | ZWMCIRCLEBY3P | CBP |
| Arc (Cen) | ZWMARCBYC | ASF |
| Arc (3P) | ZWMARCBY3P | ABP |
| Mirror line | ZWMMIRRORLINE | DMRL |
| Parallel line | ZWMPARALLELLINE | PAL |
| Vertical line | ZWMVERTICALLINE | VL |
| Tangent | ZWMTANGENTLINE | QTL |
| Common tangent | ZWMCOMMONTANGENT | CTT |
| Perpendicular bisector | ZWMPERPBISECTOR | PBS |
| Angle line | ZWMANGLELINER | AN |
| Bisector (angular bisector) | ZWMANGLEBISECTOR | AB |
| Ray | ZWMRADIATION |  |
| Center line | ZWMCENTERLINE | CL |
| Zigzag line | ZWMZIGZAGLINE |  |
| Waviness line | ZWMWAVILNESSLINE | WL |
| Rectangle | ZWMRECTANGLE | REC |
| Construction tools |
| Formula curves | ZWMFCURVE | FC |
| Fillet | ZWMFILLETAC | F |
| Chamfer | ZWMFILLETLC | CHA |
| Truncation Line | ZWMSECTIONSYMBOL | SES |
| Inserting break symbol | ZWMBREAKSYMBOL1 | BRS1 |
| Dynamic extension | ZWMDYNAMICEXTEND | DE |
| Construction line |
| Construction line | ZWMCONSTLINES | CLIN |
| Automatic construction line | ZWMAUTOCLINES |  |
| Horizontal | ZWMCONSTHOR |  |
| Vertical | ZWMCONSTVER |  |
| Cross | ZWMCONSTCRS |  |
| Two points or an angle | ZWMCONSTHB |  |
| Form a relative angle with a straight line | ZWMCONSTHW |  |
| All-distance parallel | ZWMCONSTPAR |  |
| Half distance parallel | ZWMCONSTPAR2 |  |
| Perpendicular to the connection between two points | ZWMCONSTLOT2 |  |
| Perpendicular to a straight line | ZWMCONSTLOT |  |
| Bi-section line | ZWMCONSTHM |  |
| Through point ray | ZWMCONSTXRAY |  |
| Through point straight line | ZWMCONSTXLINE |  |
| Z direction | ZWMCONSTZ |  |
| Construction circle |
| Construction circle | ZWMCONSTCIRCLE |  |
| Parallel construction line tangent to the circle | ZWMCONSTTAN |  |
| Construction line tangent to two circles | ZWMCONSTTC |  |
| Construction line concentric with a circular | ZWMCONSTCC |  |
| Construction line of end line of axis | ZWMCONSTCCREA |  |
| Construction circle tangent to a straight line | ZWMCONSTC2 |  |
| Construction circle tangent to two straight lines | ZWMCONSTKR |  |
| Rectangular construction line externally tangent to a circle | ZWMCONSTCIRCLI |  |
| HoleAxis projection | ZWMHSPROJECTOR | HSP |
| Process Tank Structure | ZWMCONSTRECESS | CSR |
| Single-hole | ZWMSINGLEHOLE | SHO |
| Hole array | ZWMARRAYHOLE | AH |
| Aids |
| convert proxy entity to blcock | ZWMPROXYTOBLOCK |  |
| Super Edit | ZWMSUPEREDIT | V |
| Area calculation | ZWMAREA | AA |
| Power Recall | ZWMPOWERRECALL |  |
| Power Erase | ZWMPOWERERASE |  |
| Tabular data pick up | ZWMTABLEDATAPICKUP | TB |
| Dwg Data Pickup | ZWMDWGDATAPICKUP |  |
| Find and Replace Text | ZWMDWGDATAFINDREPLACE |  |
| Jigsaw Print | ZWMJIGSAWPRINT | JS |
| Layer transform tool | ZWMCHGLAYER |  |
| Part Builder | ZWM_SPART_OUT | PB |
| Component Design |
| Shaft Design | ZWMSHAFT |  |
| Gear design | ZWMGEAR |  |
| Super-symbol library |
| Invocation of super symbol library | ZWM_SYMOUT | FH |
| Hydraulic and pneumatic symbol library |  | YQFH |
| Electrical symbol library |  | DQFH |
| Mechanism symbol |  | JGFH |
| Metal structural member |  | JSFH |
| System maintenance tools |
| Style Configuration | ZWMSTYLEMANAGER |  |
| Word library | ZWMWORDLIBMNG |  |
| Define Title Block | ZWMTITLEDEFINE |  |
| Define Additional Block | ZWMFJLDEFINE |  |
| Define Paralist | ZWMCSLDEFINE |  |
| Define Drawing Code Block | ZWMREVERSEDEFINE |  |
| Define Attblock | ZWMATTBLOCKDEF |  |
| Define Bom Head | ZWMBOMHEADDEFINE |  |
| Define Bom Body | ZWMBOMBODYDEFINE |  |
| Irregular Table Pickup Configuration | ZWMTBLDATAPICKUPTITCONFIG |  |
| 2D Table Pickup Configuration | ZWMTBLDATAPICKUPBOMCONFIG |  |

Note: Proficiency with the commands above will greatly help your work efficiency. It is suggested to grasp one or two-letter commands before go for the longer ones. This is also a good opportunity to exercise the left-handed applications and operations.